Parts list
This is the parts list for v1.2 ONLY! If you have a v1.0 or v1.1 kit this list will be incorrect! See below for the v1.0/v1.1 parts list guide
Check to make sure your kit comes with the following parts.Sometimes we make mistakes so double check everything and email support@adafruit.com if you need replacements!
Image	Name	Description	More info	Qty
	IC1	Microcontroller (preprogrammed when purchased in a kit)	ATTINY85V-10-PU / (unprogrammed when not purchased from Adafruit)	1
	IC1'	8-pin socket	Generic	1
	XTL1	8.00 MHz ceramic oscillator. It might also be blue.	8mhz ceramic resonator	1
	C1	220uF or higher capacitor with 6.3V or higher rating	Electrolytic Capacitor	1
	C2	Ceramic 0.1uF capacitor (104)	Ceramic Capacitor	1
	R2	1/4W 5% 10K resistor / For EU configuration use! / Brown, Black, Orange, Gold	Generic Resistor	1
	R1, R3	1.0Kohm 1/4W 5% resistor (brown black red gold)	Generic Resistor	2
	LED3, LED4	Narrow beam IR LED. These have a blue-ish tint.	Everlight IR333-A	2
	LED2, LED5	Wide beam IR LED	Everlight IR333C/H0/L10	2
	LED1	3mm LED	3mm green diffused	1
	SW1	6mm tact switch button	6mm tact switch	1
	Q1	PNP transistor, EBC pinout / Such as PN2907 or 2N3806	PN2907	1
	Q5 Q2 Q3 Q4	NPN Transistor (TO-92) that is pin compatible with 2N3904 EBC pinout	PN2222	4
	ICSP	6 pin header, 0.1"x0.1" spacing	2x3 header	1
	BATT	2 x AA battery holder	Keystone 2463	1
	PCB	Circuit board	Adafruit Industries	1